## Slide 1: Probabilistic Robotics
Probabilistic Motion Models

## Slide 2: Robot Motion
Robot motion is inherently uncertain.
How can we model this uncertainty?

## Slide 3: Dynamic Bayesian Network for Controls, States, and Sensations

## Slide 4: Probabilistic Motion Models
To implement the Bayes Filter, we need the transition model p(x | x’, u).
The term p(x | x’, u) specifies a posterior probability, that action u carries the robot from x’ to x.
In this section we will specify, how p(x | x’, u) can be modeled based on the motion equations.

## Slide 5: Coordinate Systems
In general the configuration of a robot can be described by six parameters.
Three-dimensional cartesian coordinates plus three Euler angles pitch, roll, and tilt.
Throughout this section, we consider robots operating on a planar surface.
The state space of such systems is three-dimensional (x,y,).

## Slide 6: Typical Motion Models
In practice, one often finds two types of motion models:
  Odometry-based
  Velocity-based (dead reckoning)
Odometry-based models are used when systems are equipped with wheel encoders.
Velocity-based models have to be applied when no wheel encoders are given.
They calculate the new pose based on the velocities and the time elapsed.

## Slide 7: Example Wheel Encoders
These modules require +5V and GND to power them, and provide a 0 to 5V output. They provide +5V output when they "see" white, and a 0V output when they "see" black.
These disks are manufactured out of high quality laminated color plastic to offer a very crisp black to white transition. This enables a wheel encoder sensor to easily see the transitions.
Source: http://www.active-robots.com/

## Slide 8: Dead Reckoning
Derived from “deduced reckoning.”
Mathematical procedure for determining the present location of a vehicle.
Achieved by calculating the current pose of the vehicle based on its velocities and the time elapsed.

## Slide 9: Reasons for Motion Errors
bump
ideal case
different wheel diameters
carpet
and many more …

## Slide 10: Odometry Model
Robot moves from to .
Odometry information .

## Slide 11: The atan2 Function
Extends the inverse tangent and correctly copes with the signs of x and y.

## Slide 12: Noise Model for Odometry
The measured motion is given by the true motion corrupted with noise.

## Slide 13: Typical Distributions for Probabilistic Motion Models
Normal distribution
Triangular distribution

## Slide 14: Calculating the Probability (zero-centered)
For a normal distribution
For a triangular distribution
Algorithm prob_normal_distribution(a,b):
return
Algorithm prob_triangular_distribution(a,b):
return

## Slide 15: Calculating the Posterior Given x, x’, and u
Algorithm motion_model_odometry(x,x’,u)
return p1 · p2 · p3
odometry values (u)
values of interest (x,x’)

## Slide 16: Application
Repeated application of the sensor model for short movements.
Typical banana-shaped distributions obtained for 2d-projection of 3d posterior.
x’
u
p(x|u,x’)
u
x’

## Slide 17: Sample-based Density Representation

## Slide 18: Sample-based Density Representation

## Slide 19: How to Sample from Normal or Triangular Distributions?
Sampling from a normal distribution
Sampling from a triangular distribution
Algorithm sample_normal_distribution(b):
return
Algorithm sample_triangular_distribution(b):
return

## Slide 20: Normally Distributed Samples
106 samples

## Slide 21: For Triangular Distribution
103 samples
104 samples
106 samples
105 samples

## Slide 22: Rejection Sampling
Sampling from arbitrary distributions
Algorithm sample_distribution(f,b):
repeat
until ( )
return

## Slide 23: Example
Sampling from

## Slide 24: Sample Odometry Motion Model
Algorithm sample_motion_model(u, x):
Return
sample_normal_distribution

## Slide 25: Sampling from Our Motion Model
Start

## Slide 26: Examples (Odometry-Based)

## Slide 27: Velocity-Based Model

## Slide 28: Equation for the Velocity Model
Center of circle:
with

## Slide 29: Posterior Probability for Velocity Model

## Slide 30: Sampling from Velocity Model

## Slide 31: Examples (velocity based)

## Slide 32: Map-Consistent Motion Model

Approximation:

## Slide 33: Summary
We discussed motion models for odometry-based and velocity-based systems
We discussed ways to calculate the posterior probability p(x| x’, u).
We also described how to sample from p(x| x’, u).
Typically the calculations are done in fixed time intervals t.
In practice, the parameters of the models have to be learned.
We also discussed an extended motion model that takes the map into account.